## Slide 1: Magnetometer Calibration
2 Wheels 2 Furious
Scott Clemens

## Slide 2: Raw Magnetometer Data
Circular and offset from origin
Origin is the black dot.
Oval and offset from origin
Circular and offset from origin
BEFORE CALIBRATION

## Slide 3: Combined Raw Data
Three axis are not aligned due to offsets in raw values. Ideal outcome is to have three overlapping circles with center at the origin.
BEFORE CALIBRATION
Origin is the black dot.
X data max = 0.744 min = -0.168 range = 0.912 average = 0.262
Y data max = 0.815 min = -0.137 range = 0.952 average = 0.276
Z data max = -0.024 min = -0.979 range = 0.956 average = -0.462
X-Y data h = 0.295 k = 0.35 a = 0.285 b = 0.291 a/b = 0.98
Y-Z data h = 0.336 k = -0.513 a = 0.288 b = 0.294 a/b = 0.979
Z-X data h = -0.518 k = 0.304 a = 0.29 b = 0.281 a/b = 1.031

## Slide 4: Raw Heading Data
BEFORE CALIBRATION
Rollover present due to proximity to +180 degrees

## Slide 5: Combined Heading Data
BEFORE CALIBRATION

## Slide 6: Initial Calibration Method
Add/subtract average value in real-time to raw values to shift magnetometer circle center to origin

## Slide 7: Raw Magnetometer Data
INITIAL CALIBRATION
Origin is the black dot.
Circular and slight offset from origin
Oval and slight offset from origin
Circular and slight offset from origin

## Slide 8: Combined Raw Data
Origin is the black dot.
Three axis are better aligned due to correction of offsets in raw values.
X data max = 0.494 min = -0.405 range = 0.899 average = 0.043
Y data max = 0.503 min = -0.426 range = 0.929 average = 0.02
Z data max = 0.444 min = -0.52 range = 0.964 average = 0.051
X-Y data h = 0.062 k = 0.056 a = 0.271 b = 0.292 a/b = 0.928
Y-Z data h = 0.058 k = -0.059 a = 0.297 b = 0.301 a/b = 0.985
Z-X data h = -0.043 k = 0.029 a = 0.293 b = 0.279 a/b = 1.051
INITIAL CALIBRATION
All h and k values (center) are closer to 0

## Slide 9: Combined Heading Data
INITIAL CALIBRATION
No more rollover present due to shifting raw values

## Slide 10: Final Calibration Method
2. Scale data by ratio of i_range to average of j_range and k_range values
X_range/[(Y_range + Z_range)/2] = 0.949
Y_range/[(Z_range + X_range)/2] = 0.997
Z_range/[(X_range + Y_range)/2] = 1.0547

## Slide 11: Payload Raw Data
BEFORE CALIBRATION

## Slide 12: Payload Raw Data
X data max = 0.463 min = -0.419 range = 0.881 average = -0.004
Y data max = 0.506 min = -0.435 range = 0.942 average = 0.026
Z data max = 0.442 min = -0.458 range = 0.9 average = 0.037
X-Y data h = 0.036 k = 0.03 a = 0.264 b = 0.296 a/b = 0.893
Y-Z data h = 0.042 k = -0.017 a = 0.304 b = 0.279 a/b = 1.09
Z-X data h = -0.026 k = 0.044 a = 0.281 b = 0.284 a/b = 0.99
BEFORE CALIBRATION

## Slide 13: Payload Raw Data
AFTER CALIBRATION

## Slide 14: Payload Raw Data
X data max = 0.544 min = -0.444 range = 0.988 average = 0.082
Y data max = 0.453 min = -0.439 range = 0.892 average = 0.023
Z data max = 0.412 min = -0.51 range = 0.922 average = -0.032
X-Y data h = 0.055 k = -0.004 a = 0.304 b = 0.277 a/b = 1.095
Y-Z data h = 0.001 k = -0.05 a = 0.276 b = 0.285 a/b = 0.969
Z-X data h = -0.043 k = 0.055 a = 0.276 b = 0.292 a/b = 0.944
X data max = 0.463 min = -0.419 range = 0.881 average = -0.004
Y data max = 0.506 min = -0.435 range = 0.942 average = 0.026
Z data max = 0.442 min = -0.458 range = 0.9 average = 0.037
X-Y data h = 0.036 k = 0.03 a = 0.264 b = 0.296 a/b = 0.893
Y-Z data h = 0.042 k = -0.017 a = 0.304 b = 0.279 a/b = 1.09
Z-X data h = -0.026 k = 0.044 a = 0.281 b = 0.284 a/b = 0.99
AFTER CALIBRATION